## Slide 1
Tools and Equipments
used for Apparel Construction
Presented by,
Dr. Ila Jogi
Mahila Mahavdyalaya, Karad

## Slide 2
In the present day culture, sewing has become mostly a mass manufacturing trade.
Sewing tools and equipments are needed for sewing which aid in construction of garments of good quality and appearance.
Sewing equipment and tools will visualise the use of different tools used in apparel construction. A good knowledge of these tools help in using the appropriate tool for overall quality of the product prepared besides making the task of easy for the beginner.
The equipments and tools are broadly categorized into Measuring, Drafting, Marking, Cutting, Sewing and Pressing tools. A box with compartment is necessary to arrange these tools in one place.

## Slide 3
Why is it important to know the tools and equipment used in sewing?
The importance of defining the tools and equipment in sewing is two-fold.
First, it will give you a way to calculate startup costs and,
Secondly, in learning the functions of sewing tools and equipment, you will be able to define exactly what sort of duties a person in this industry performs.

## Slide 6
Classification of Sewing Tools and Equipment and Their Uses
Some of the basic tools and equipment available to the sewer are:
Measuring tools, Tracing tools, Drafting tools, Cutting tools, Pinning and Sewing tools, and others.
Measuring Tools- Measuring tape, Meter scale, Ruler, L Square, French curve
Marking/Tracing Tools- Tailor’s chalk, Tracing Wheel, Tailor’s pencil, Carbon Paper, Liquid Marking Pencil, Tracing Paper, Colour Pencil (Red and Blue)
Drafting Tools- Wooden table, Brown paper, Dress Model, Bell pin, Pin cushions
Cutting Tools- Scissors, Shears, Pinking Shears, Seam Ripper, Thread Clipper, Embroidery Scissors
Sewing Tools- Fabric, Needles, Thread, Thimble, Needle Threader, Bodkin, Loop Turner
Pressing Tools- Steam/Dry Iron, Ironing Board, Press Cloth, Sleeve Board, Seam Roll, Steam Press

## Slide 7
Basic Measuring Tools:

## Slide 8: Tape Measure
Long plastic or fiberglass strip with marks for measuring:
1. Fabric
2. patterns
Body Measurements
A tape measure can also measure up to great distances.

## Slide 9: Measuring Tape
It is 152 cm or 60″ long with measurements on both sides.
Its one end is made of metal having 3″ length and the other is made of the same metal having 1/2″ length.
The side with the 1/2″ length is used for measuring a circular area, while the side with 3″ length is used for a vertical area.

## Slide 10: Seam gauge
Seam gauges are
Small metal rulers
Used to measure small areas
6 inch ruler with a sliding marker, used to measure short distances.
A sewing gauge or hem gauge are a couple of different tools used
to measure short distances. They are only 6” long, so are commonly used for hemming.

## Slide 11: Hem Gauge
Multipurpose measuring tool.
It has a curved, hem-shaped side that is used to mark standard hem depths
Straight side is used like a ruler
A sewing gauge or hem gauge used to measure short distances. They are only 6” long, so are commonly used for hemming.

## Slide 12: Yard Stick
Wooden measuring stick.
Usually a yard or a meter long
A yardstick can be used for measuring straight, longer distances and for checking grain lines.

## Slide 13: Measuring stand
Measuring stand: This stand is used to measure long garments such as long overcoats, frocks or gowns, as well as flare of the garment. In this stand, a rod of aluminium is fitted on the stand. The rod has a graduated scale, which gives the vertical measurement.

## Slide 15: Drafting Tools
Drafting equipment is used for making paper patterns. This is the second stage of pattern making. Using the measurements taken, the drafting is carried out according to the design of a garment. The following drafting equipment is used:
L-scale: It is called a triscale or L-scale and is made of wood or steel. The L-scale has one arm, which measures 12″ and the other arm is 24″. It is used for drafting on brown paper to draw perpendicular lines.
Leg shaper: It is made of wood or plastic. Either 24″ or 36″ lengths are available. It is used to measure and shape the interior part of the leg
Tailor’s art curve: It is made of plastic or wood. This is used to draw curves in the drafting.
French curve: This is made of transparent plastic. It helps in marking shapes of the neck, depth of sides and bottom of the garments.
Compass: It is mainly used for making a curve for umbrella cloth.
Drafting table: It is a wooden table of 3′ height, 4′ wide and 6′ long. The surface should be smooth and firm.

## Slide 16: Drafting Tools
Milton cloth: It is a thick, blue coloured woolen cloth used for drafting. It is mostly used for practising drafts by students. The surface can be brushed and reused until correct drafting is obtained.
Brush: A brush is used on Milton cloth to rub the mistakes while drafting.
Brown paper: It is used for drafting by placing on the drafting table. While using brown paper, a grain line should be followed.
Pencil: Pencil is used for marking on brown paper.
Rubber: It is frequently used for deleting mistakes. Good quality rubber, which does not leave black lines, should be selected.
Sewing table: Sewing table is necessary for laying out your patterns, fabrics, and for keeping your tools all in one place.
You might prefer a table that can be lowered or raised, depending on whether you prefer to sit or stand.

## Slide 17: Marking Tools
Tracing wheel
Tailor’s pencil
Tailor’s chalk
Tracing paper
  All used to transfer pattern markings to the fabric

## Slide 18
Basic tracing tools:
Tailor’s chalk and a chalk pencil are used for marking directly on the fabric and can easily be brushed off when the work is complete.
A tracing wheel, whether serrated or smooth, can be rolled onto fabrics to create designs and lines.
Carbon paper, a wax-papery material, lays under the tracing wheel and transfers the design from the wheel to the fabric.
A liquid marking pen does the same job as chalk, but it comes in a variety that can be washed out or one that fades within a 48 hour period of time. After marking your design or fabric, the right cutting tools are necessary to make the perfect pattern and garment.
Disappearing Ink Pen : The ink will disappear by evaporating after a certain time, or you can remove it with a damp cloth. Test the ink on your fabric, especially on silk.

## Slide 19: Marking Pencils & Pens
Special pens or pencils that are used to mark fabric when sewing

## Slide 20: Tracing Wheel and Paper
Coated paper comes in assorted colors
Used to transfer markings onto fabric

## Slide 21: Tailor’s Chalk
Used to transfer markings onto fabric
Remove them by brushing before pressing over them.
Can easily be brushed off when the work is complete.

## Slide 22
Cutting Tools

## Slide 23: Cutting Tools
Shears
  Longer than scissors
  Bent handle allows fabric to lie flat as it is cut
  Used to cut fabric
  Bent handled shears are made from a high-quality steel that maintains a sharp cutting edge. The 7-12” blades move quite smoothly, cutting the full length of the blades, and they can be used on almost any fabric.

## Slide 24: Cutting Tools
Scissors
  Usually short
  Used to trim seams and threads

## Slide 25: Cutting Tools
Pinking Shears
  Zig zag cutting edge
  Used to give seam edges a finished look
  Prevent raveling
  Give a decorative edge

## Slide 26: Embroidery Scissors
Small sharp scissors for trimming threads
And cutting in small places

## Slide 27: Buttonhole Scissors
Special scissors that help you cut the slit for the button hole

## Slide 28: Thread Clips
Used to clip the
threads as you sew
Thread clippers are a handy little spring-loaded tool that cuts thread.

## Slide 29: Scissor Rules
Cut only fabric
Never cut pins
Don’t drop
Get sharpened when dull
Dull scissors will not cut fabric!

## Slide 30: Rotary Cutter
Used to cut fabric
Looks like pizza cutter
For fabric

## Slide 31: Rotary Ruler and Mat
The ruler is used with the rotary cutter
To cut straight.
The mat is a special
Mat that protects the table.

## Slide 32: Danger!
You can be seriously hurt by the blade of the rotary cutter!
The blade is a razor blade and very sharp!
If you cannot use the rotary cutter safely, you will not be able to use it any more

## Slide 33: Seam Ripper
A small sharp tool
Used to remove stitches
Seam ripper is a way to remove thread that is sewn into any fabric without tearing the fabric.

## Slide 34: Cutting Tools
Seam ripper
  Used to undo mistakes
  Has a sharp edge!
  a seam ripper is a way to remove thread that is sewn into any fabric without tearing the fabric.

## Slide 35
Pinning and Sewing Tools

## Slide 36
Sewing Machine: It is a machine used to stitch fabric and other materials together with thread. There are various types of sewing machines.

## Slide 37
Needles are the actual sewing tool. When threaded, a needle binds the thread to the fabric thus holding your creation together.

## Slide 38: Sewing Tools
Pins
  Used to hold fabric together before sewing
  Take the pins out as you sew

## Slide 39: Sewing Tools
Thimble
  Protects your finger while sewing by hand
  A thimble serves as a guard for the finger that pushes the needle when sewing;

## Slide 40: Sewing Tools
Magnetic Pin Holder/Pin cushion
  Store pins
  A pincushion holds bare pins and needles for easy grabbing, keeps them in one place neatly, and helps to prevent accidents.

## Slide 41: Sewing Tools
Thread
  Comes in a variety of colors
  Match the thread color to the color of your fabric
  Needles are the actual sewing tool. When threaded, a needle binds the thread to the fabric thus holding your creation together.

## Slide 42: Sewing Tools
Bobbin
  Empty spindle for thread
  Your thread color needs to match your bobbin color

## Slide 43: Loop Turner
Long slim wire with a latch hook at one end used to turn tubing or cording to the right side

## Slide 44: Point Turner
Plastic or wooden point turner used to push out points such as collars and cuffs

## Slide 45: Bodkin
Used for inserting elastic or drawstrings into casings

## Slide 46
Iron:
An iron is a tool used to remove wrinkles from fabric before, during and after sewing. A good brand with after sale services should be chosen. A steam iron with a thermostat regulator is preferred.
Pressing Tools

## Slide 47
An ironing board allows fabrics and garments to be freely ironed and is designed to handle the heat of an iron. For ironing clothes, a table or ironing board can be used. An ironing board is 36″ long and 12″ wide. Six inches are left on its right side to keep the iron box. The left side of the board is angular and is suitable for ironing dart edges and sleeve darts while stitching. The table or ironing board should have proper stuffed backing
Ironing Board
Sleeve Board: Used for pressing sleeve and small. It is in the shape of a sleeve. This board is 30″ long and 3/4″ thick

## Slide 48
Press Cloth- A simple white cloth that is laid between your iron and your garment to help protect from the iron’s heat.
Seam Roll: A pressing tool helpful in pressing smaller curved seams. It makes pressing darts and small seams easier as well as zippers and small some areas of collars

## Slide 49
Thank you…